## Slide 1: Extending the Scope of Algebraic MINLP Solvers to Black- and Grey-box Optimization
Nick Sahinidis
Acknowledgments:
Alison Cozad, David Miller, Zach Wilson

## Slide 2: SIMULATION OPTIMIZATION
Pulverized coal plant Aspen Plus® simulation provided by the National Energy Technology Laboratory
Notes: Simulation optimization is a very attractive option when it comes to optimizing complicated processes. High fidelity simulations can often represent real world systems with extremely high accuracy. When it comes to optimizing over these simulations, the effort and structure required to achieve this high accuracy can cost advanced optimizers speed and rigorous solutions.
The primary challenges in optimizing over any black-box process are:
-First, the absence of an algebraic model. I will explain a bit more about why this is a particularly large challenge later.
-Costly simulations, this could be the cost of raw materials for an experimental set up, or the minutes, hours, or days it can take for a simulations to converge.
-In many cases, these simulations can have noise associated with them.
-Oftentimes, a simulation cannot converge to new points without manual manipulation .

## Slide 3: Process disaggregation
Block 1:
Simulator
Model generation
Block 2:
Simulator
Model generation
Block 3:
Simulator
Model generation
Surrogate Models
Build simple and accurate models with a functional form tailored for an optimization framework
Process Simulation
Disaggregate process into process blocks
Optimization Model
Add algebraic constraints design specs, heat/mass balances, and logic constraints

## Slide 4: LEARNING Problem
Build a model of output variables as a function of input variables x over a specified interval
Independent variables:
Operating conditions, inlet flow properties, unit geometry
Dependent variables:
Efficiency, outlet flow conditions, conversions, heat flow, etc.
Process simulation or Experiment
Notes: - Automated learning of algebraic models for optimization
Tasked w/ fundamental problem of learning al algebraic model from a black box simulation given I/O data

## Slide 5: How to build the surrogates
We aim to build surrogate models that are
  Accurate
    We want to reflect the true nature of the simulation
  Simple
    Tailored for algebraic optimization
  Generated from a minimal data set
    Reduce experimental and simulation requirements
Notes: There has been work done to abstract surrogate models from simulators then use them for optimization. Most of these methods use out of the box modeling techniques that, while accurate, can be often cumbersome or intractable in algebraic optimization.
We have developed our own modeling scheme with the aim of developing models that are:
First and foremost, accurate
To address the ease of the final optimization, we tailor the functional form and complexity of our model such that it can be tractably solved. By this, I mean that if we would like to represent the system with a small set of simple basis functions instead of larger more complex models that may arise from methods such as Kriging, Neural networks, radial basis functions, etc.
We would also like to reduce our modeling time by using as few costly simulation function evaluations as possible.

## Slide 6: ALAMO
Automated Learning of Algebraic Models for Optimization
true
Stop
Update training data set
Start
false
Initial sampling
Build surrogate model
Adaptive sampling
Model converged?
Black-box function
Initial sampling
Build surrogate model
Current model
Model
error
Adaptive sampling
Update training data set
New model

## Slide 7: Model complexity tradeoff
Kriging [Krige, 63]
Neural nets [McCulloch-Pitts, 43]
Radial basis functions [Buhman, 00]
Model complexity
Model accuracy
Linear response surface
Preferred region

## Slide 8: Model identification
Goal: Identify the functional form and complexity of the surrogate models
Functional form:
  General functional form is unknown: Our method will identify models with combinations of simple basis functions

## Slide 9: Overfitting and true error
Step 1: Define a large set of potential basis functions
Step 2: Model reduction
True error
Empirical error
Complexity
Error
Ideal Model
Overfitting
Underfitting

## Slide 10: Model reduction techniques
Qualitative tradeoffs of model reduction methods
CPU modeling cost
Efficacy
Backward elimination [Oosterhof, 63]
Forward selection [Hamaker, 62]
Stepwise regression [Efroymson, 60]
Regularized regression techniques
  Penalize the least squares objective using the magnitude of the regressors [Tibshirani, 95]
Best subset methods
    Enumerate all possible subsets

## Slide 11: Model sizing
Complexity = number of terms allowed in the model
Goodness-of-fit measure
6th term was not worth the added complexity
Final model includes 5 terms
Some measure of error that is sensitive to overfitting
(AICc, BIC, Cp)
Solve for the best one-term model
Solve for the best two-term model

## Slide 12: Basis function selection
Find the model with the least error
We will solve this model for increasing T until we determine a model size

## Slide 13: ALAMO
Automated Learning of Algebraic Models for Optimization
true
Stop
Update training data set
Start
false
Initial sampling
Build surrogate model
Adaptive sampling
Model converged?
Model
error
Error maximization sampling

## Slide 14: Error maximization sampling
Search the problem space for areas of model inconsistency or model mismatch
Find points that maximize the model error with respect to the independent variables
  Derivative-free solvers work well in low-dimensional spaces [Rios and Sahinidis, 12]
  Optimized using a black-box or derivative-free solver (SNOBFIT) [Huyer and Neumaier, 08]
Surrogate model

## Slide 15: Computational results
Goal – Compare methods on three target metrics
Modeling methods compared
  ALAMO modeler – Proposed methodology
  The LASSO – The lasso regularization
  Ordinary regression – Ordinary least-squares regression
Sampling methods compared (over the same data set size)
  ALAMO sampler – Proposed error maximization technique
  Single LH – Single Latin hypercube (no feedback)
Model simplicity
3
Data efficiency
2
Model accuracy
1

## Slide 16
Fraction of problems solved
Ordinary regression
ALAMO modeler
the lasso
Ordinary regression
ALAMO modeler
the lasso
(0.005, 0.80)
80% of the problems had ≤0.5% error
70% of problems solved exactly
Normalized test error
error maximization sampling
single Latin hypercube
Model simplicity
3
Data efficiency
2
Model accuracy
1
Normalized test error
Notes: ALAMO models able to solve exactly 70%, 67% of the time
EMS is able to ‘repair’ the lasso and OLR methods through repeated sampling given the same data set size

## Slide 17
ALAMO sampler
Single LH
ALAMO sampler
Single LH
ALAMO sampler
Single LH
Ordinary regression
ALAMO modeler
the lasso
Normalized test error
Fraction of problems solved
Model simplicity
3
Data efficiency
2
Model accuracy
1

## Slide 18
more complexity than required
Results over a test set of 45 known functions treated as black boxes with bases that are available to all modeling methods.
Modeling type, Median
Model simplicity
3
Data efficiency
2
Model accuracy
1

## Slide 19: MODEL SELECTION CRITERIA
Balance fit (sum of square errors) with model complexity (number of terms in the model; denoted by p)
Corrected Akaike Information Criterion
Mallows’ Cp
Hannan-Quinn Information Criterion
Bayes Information Criterion
Mean Squared Error

## Slide 20: CPU TIME Comparison
Chart: Problem Size
| 20 | 50 | 60 | 70 | 80
Cp | 0.05 | 57 | 800 | 4884 | 9791
BIC | 0.02 | 7 | 28 | 111 | 328
AIC, MSE, HQC | 0.5 | 641 | 4428 | 33488 | 82815
Eight benchmarks from the UCI and CMU data sets
Seventy noisy data sets were generated with multicolinearity and increasing problem size (number of bases)
BIC solves more than two orders of magnitude faster than AIC, MSE and HQC
  Optimized directly via a single mixed-integer convex quadratic model

## Slide 21: MODEL QUALITY Comparison
Chart: Problem Size
| 20 | 50 | 60 | 70 | 80
Cp | 3.1 | 6.6 | 6.6 | 9.3 | 8.8
BIC | 0.4 | 1.3 | 0.3 | 0.5 | 0
AIC | 3 | 6.5 | 6.4 | 9.4 | 10.3
HQC | 3 | 5.5 | 4.5 | 6 | 5.3
MSE | 6.1 | 14.5 | 18.8 | 22 | 21.8
Chart: Problem Size
| 20 | 50 | 60 | 70 | 80
Cp | 8.2 | 5.49 | 3.49 | 5.36 | 4.78
BIC | 6 | 3.88 | 2.05 | 1.93 | 2.87
AIC | 8.25 | 5.49 | 3.47 | 6.55 | 4.6
HQC | 8.52 | 5.42 | 3.33 | 4.81 | 3.95
MSE | 9.07 | 6.79 | 5.09 | 6.94 | 5.79
BIC leads to smaller, more accurate models
  Larger penalty for model complexity

## Slide 22: ALAMO remarks
Expanding the scope of algebraic optimization
  Using low-complexity surrogate models to strike a balance between optimal decision-making and model fidelity
Surrogate model identification
  Simple, accurate model identification – Integer optimization
Error maximization sampling
  More information found per simulated data point
Rebuild model
Error maximization
New surrogate model
Surrogate model

## Slide 23: THEORY utilization
Use freely available system knowledge to strengthen model
  Physical limits
  First-principles knowledge
  Intuition
Non-empirical restrictions can be applied to general regression problems
empirical data
non-empirical information

## Slide 24: Constrained regression
Challenging due to the semi-infinite nature of the regression constraints
Standard regression
Surrogate model
easy
tough
Notes: Use intuitive restrictions among predictor and response variables to imply nonintuitive relationships between regression parameters

## Slide 25: Implied parameter restrictions
Step 1: Formulate constraint in z- and x-space
Step 2: Identify a sufficient set of β-space constraints
1 parametric constraint
4 β-constraints

## Slide 26: Types of Restrictions
Multiple responses
Individual responses
Response bounds
Response derivatives
Alternative domains
Boundary conditions
Multiple responses
mass balances, sum-to-one, state variables
Individual responses
mass and energy balances, physical limitations
Response bounds
pressure, temperature, compositions
Response derivatives
Alternative domains
Boundary conditions
monotonicity, numerical properties, convexity
safe extrapolation, boundary conditions
Add
no slip
velocity profile model
safe extrapolation, boundary conditions
Problem Space
Extrapolation zone

## Slide 27: CARBON CAPTURE SYSTEM DESIGN
Discrete decisions: How many units? Parallel trains?
What technology used for each reactor?
Continuous decisions: Unit geometries
Operating conditions: Vessel temperature and pressure, flow rates, compositions
Surrogate models for each reactor and technology used

## Slide 28: SUPERSTRUCTURE OPTIMIZATION
Mixed-integer nonlinear programming model
  Economic model
  Process model
    Material balances
    Hydrodynamic/Energy balances
    Reactor surrogate models
  Link between economic model and process model
  Binary variable constraints
  Bounds for variables

## Slide 29: GLOBAL MINLP SOLVERS on cmu/ibmlib
BARON 13
LINDOGLOBAL
BARON 14
COUENNE
SCIP
ANTIGONE

## Slide 30: conclusions
ALAMO provides algebraic models that are
  Accurate and simple
  Generated from a minimal number of function evaluations
ALAMO’s constrained regression facility allows modeling of
  Bounds on response variables
  Convexity/monotonicity of response variables
On-going efforts
    Uncertainty quantification
    Symbolic regression
ALAMO site: archimedes.cheme.cmu.edu/?q=alamo